## Slide 1
CYBERTRAFFIC AI
AI-Enhanced Fuzzy Controller for Smart Traffic Management
BE05000461 — Fuzzy Logic and Genetic Programming
L.D. College of Engineering • Computer Engineering Department • Smart Cities
Project Presentation
CYBERTRAFFIC AI • Smart Traffic Management 1

## Slide 2
1. Problem Statement
Why fixed-time traffic signals are inefficient
OFF-PEAK
Vehicles may wait unnecessarily at empty intersections because signal timings remain fixed.
RUSH HOURS
Fixed timers may fail to clear heavy queues quickly, increasing congestion and delay.
EMERGENCIES
Traditional systems do not inherently detect emergency vehicles or adapt to live incidents.
Proposed solution: Intelligent Traffic Management System (ITMS).
Mamdani Fuzzy Inference System calculates green-light duration from real-time traffic data.
AI and computer vision provide live traffic-state inputs and emergency override capability.
CYBERTRAFFIC AI • Smart Traffic Management 2

## Slide 3
2. Objectives
01
Model the vague, dynamic nature of urban traffic using fuzzy logic.
02
Design linguistic variables, membership functions and a robust rule base.
03
Implement the Mamdani fuzzy inference system using Python and scikit-fuzzy.
04
Conceptualize AI computer vision for queue length and waiting-time estimation.
05
Evaluate controller performance through testing and simulation.
CYBERTRAFFIC AI • Smart Traffic Management 3

## Slide 4
3. Advanced AI Integration Architecture
AI modules collect and interpret live traffic information before fuzzy control
CCTV / IoT
Live traffic data
Computer Vision
YOLO detects, classifies & tracks vehicles
Traffic State
Queue length + waiting time
Mamdani Fuzzy Controller
9-rule decision engine
Traffic Signal
Adaptive green duration
Emergency Vehicle Preemption (EVP)
Visual/audio recognition can override the fuzzy cycle and trigger an emergency “green wave.”
Predictive Analytics
Historical + IoT data can predict peak congestion and pre-adjust fuzzy rule weights.
CYBERTRAFFIC AI • Smart Traffic Management 4

## Slide 5
4. Fuzzy Controller — Inputs & Output
Two traffic-state inputs determine adaptive green-light duration
INPUT 1 — QUEUE LENGTH
0–50 vehicles Low • Medium • High
INPUT 2 — WAITING TIME
0–10 minutes Short • Medium • Long
OUTPUT — GREEN DURATION
10–90 seconds Short • Medium • Long
Variable
Set
Triangular MF
Queue
Low
(0, 0, 25)
Queue
Medium
(0, 25, 50)
Queue
High
(25, 50, 50)
Wait
Short
(0, 0, 5)
Wait
Medium
(0, 5, 10)
Wait
Long
(5, 10, 10)
Duration
Short
(10, 10, 50) → center 20s
Duration
Medium
(10, 50, 90) → center 50s
Duration
Long
(50, 90, 90) → center 80s
CYBERTRAFFIC AI • Smart Traffic Management 5

## Slide 6
5. Fuzzy Rule Base
Nine heuristic IF–THEN rules emulate human traffic-control reasoning
Queue \ Wait
Short
Medium
Long
Low
SHORT
IF Low queue AND Short wait
SHORT
IF Low queue AND Medium wait
MEDIUM
IF Low queue AND Long wait
Medium
MEDIUM
IF Medium queue AND Short wait
MEDIUM
IF Medium queue AND Medium wait
LONG
IF Medium queue AND Long wait
High
LONG
IF High queue AND Short wait
LONG
IF High queue AND Medium wait
LONG
IF High queue AND Long wait
CYBERTRAFFIC AI • Smart Traffic Management 6

## Slide 7
6. Implementation & User Interface
Python + scikit-fuzzy with a Streamlit-based interactive dashboard
PYTHON STACK
NumPy • scikit-fuzzy • fuzzy control system
FUZZY ENGINE
Antecedents → membership functions → 9 rules → simulation
WEB UI
Streamlit sliders for queue length and maximum waiting time
queue = ctrl.Antecedent(np.arange(0, 51, 1), 'queue_length') wait = ctrl.Antecedent(np.arange(0, 11, 1), 'waiting_time') duration = ctrl.Consequent(np.arange(10, 91, 1), 'green_duration') queue.automf(names=['low', 'medium', 'high']) wait.automf(names=['short', 'medium', 'long']) duration.automf(names=['short', 'medium', 'long']) rule1 = ctrl.Rule(queue['low'] & wait['short'], duration['short']) rule9 = ctrl.Rule(queue['high'] & wait['long'], duration['long'])
CYBERTRAFFIC AI • Smart Traffic Management 7

## Slide 8
7. Manual Verification — Example
Crisp inputs: Queue Length = 20 vehicles, Waiting Time = 4 minutes
FUZZIFICATION
Queue: Low = 0.2, Medium = 0.8 Wait: Short = 0.2, Medium = 0.8
RULE EVALUATION
R1 = 0.2 Short R2 = 0.2 Short R4 = 0.2 Medium R5 = 0.8 Medium
DEFUZZIFICATION
Weighted average = (4 + 4 + 10 + 40) / 1.4 ≈ 41.43 seconds
Crisp output = [(0.2×20)+(0.2×20)+(0.2×50)+(0.8×50)] ÷ (0.2+0.2+0.2+0.8)
OPTIMAL GREEN ≈ 41.43 s
CYBERTRAFFIC AI • Smart Traffic Management 8

## Slide 9
8. Testing & Results
Representative test cases from the project report
Case
Queue
Wait (min)
Output (s)
System response
1
5
2
~20.00
Normal flow, minimal wait.
2
25
2
~50.00
Growing queue, immediate action.
3
5
10
~50.00
Low queue but critical wait.
4
45
10
~80.00
Extreme congestion, maximum green.
5
20
4
~41.43
Moderate traffic, balanced response.
KEY RESULT
The controller dynamically increases green duration as queue severity and waiting time rise.
CYBERTRAFFIC AI • Smart Traffic Management 9

## Slide 10
9. Strengths, Limitations & Future Scope
STRENGTHS
• Reduces the “empty intersection” problem. • Uses waiting time for fairness. • Adapts green duration to traffic conditions.
LIMITATION
• Current fuzzy controller manages an isolated intersection. • It does not consider downstream traffic conditions.
FUTURE WORK
• Multi-agent coordination / green waves • Weather & road-condition input • ANPR-based automated enforcement
01
Multi-agent coordination
02
Weather-aware control
03
ANPR enforcement
CYBERTRAFFIC AI • Smart Traffic Management 10

## Slide 11
10. Conclusion
Fuzzy Logic + AI-driven data acquisition
provides an adaptable approach to urban traffic management.
ADAPTIVE
Dynamically adjusts signal timing.
EFFICIENT
Targets lower waiting time and congestion.
EMERGENCY-READY
Supports emergency routing through override logic.
CYBERTRAFFIC AI • Smart Traffic Management 11

## Slide 12
THANK YOU
Questions & Discussion
CYBERTRAFFIC AI • Smart Traffic Management
CYBERTRAFFIC AI • Smart Traffic Management 12